## Slide 1: Neural Network for estimated line benefits

## Slide 2: Overview
Problem setting + motivation (2-3)
Methodology
  Process overview (1)
  Optimization problem (1)
  Neural network (2)
  Line benefits (1)
  Clustering process (1)
Results thus far
  Neural network output (6)
  Line benefits (2)
Future tasks (1)

## Slide 3: Problem setting
Research background
Transmission expansion planning (TEP) is based on calculating Optimal Power Flow (OPF)
OPF problem is computationally heavy, especially AC formulations
Temporal aggregation for problem size reduction
Clustering for representative periods
How to find representative days for a spatially resolved system?
Ex-post clustering
Multitude of OPFs have to be solved for Transmission Expansion Planning
  Multiple investment candidates (lines)
  Multiple discrete investment quantities
  Weather year sensitivity
Might still be computationally intensive
Literature shows that ML methods can accurately approximate OPF results very fast

## Slide 4: Background: transmission expansion planning
TEP is based on calculating the demanding OPF problem
Increasing share of renewables  Rising variability in system operation
Temporal reduction techniques  Representative periods
Capture variability in system operating conditions (weather)
Accurately represent physical constraints of network
Many demanding OPFS
Computational tractability
Temporal reduction
Representative periods

## Slide 5: Motivation: finding representative periods
How to find representative periods for a spatially resolved system with complex interactions?
 Ex-post clustering = use simplified model to extract features relevant for your problem and cluster on those

## Slide 6: Motivation: finding representative periods
Proposed feature for clustering for TEP: Investment benefit of individual lines
  Many possible candidates
  Many discrete values for expansion
  Weather year sensitivity
A multitude of OPFs to be solved
Replace part of the calculation with a machine-learning algorithm

## Slide 7: Process overview
*ESOM: Energy System Optimization Model
**ANN: Artificial Neural Network
ESOM
ESOM
Input Data
Representative Time Series
ESOM
Representative Time Series
Relaxed ESOM
Benchmark:
Full time horizon
Traditional:
Split time horizon
Based in Costs:
Split time horizon
Features
(Investment benefit)
ESOM
Representative Time Series
ANN: Cost Estimator
Proposal:
Split time horizon
Investment Benefit Method
Features
Input Time Series
(ANN + Kmedoids)
Clustering
Method
Clustering
Method
Clustering
Method

## Slide 8: ESOM: Transmission Expansion Planning considering AC-OPF
Minimize: |  |  | (1.1)
With constraints: |  |  | 
 |  |  | (1.2)
 |  |  | (1.3)
 |  |  | (1.4)
 |  |  | (1.5)
 |  |  | (1.6)
 |  |  | (1.7)
 |  |  | (1.8) (1.9)
Minimize: |  |  | (1.1)
With constraints: |  |  | 
 |  |  | (1.2)
 |  |  | (1.3)
 |  |  | (1.4)
 |  |  | (1.5)
 |  |  | (1.6)
 |  |  | (1.7)
 |  |  | (1.8) (1.9)
Non-convex

## Slide 9: Neural Network for cost estimation
Goal
Estimate the hourly operational cost of the OPF problem
Sensitive to
  time-series changes
  physical network changes
Approach
  Neural network works on hourly basis  Estimates one cost value
  Single output (cost)
  Input contains
    Demand (per node)
    Renewable availability factors (per technology per location)
    Admittance matrix
  Size of input vector quickly grows with number of buses
…
Input layer
Single output
…
…
Demands
Availabilities
Admittance matrix
Hidden layer
…
Operational cost for one hour

## Slide 10: Neural network training
Goal
Train and test on a subset of desired outcomes
Achieve speedup by obtaining remaining outcomes with NN instead of optimization
Approach
Optimization performed for
  1 week of each month
  All individual line candidates
Split obtained dataset into training and test sets
Tune network design to obtain best result on test set

## Slide 11: NN estimates: preliminary results
Estimation of operational cost for 24 bus system
Time dependency is reproduced, but predictions are not perfect
More complex networks (more hidden layers) seem to be performing better
Training set
Test set

## Slide 12: NN estimates: hyperparameter tuning
Goal
Find the optimal design and training parameters for the neural network
Approach
Train a bunch of models on the same dataset and store the loss (MSE) on the test set for all of them
Continue with model that has lowest loss
Problem
There seems to be quite some randomness

## Slide 13: NN estimates: towards line benefits
Eventually, line benefits obtained from NN must match actual line benefits
Differences between costs from different physical networks are quite small  Predictions must be extremely accurate?
Maybe not, as long as differences are well-reproduced
 Estimate line benefits directly?

## Slide 14: NN Estimates: negative values
Custom loss function

## Slide 15: Future tasks
Consider more complex networks: more hidden layers
Use physics-informed loss function: prevent negative costs (WIP)
Extending or changing the used data:
  More input hours/line expansions
  Consider other outputs than operational costs
    Line utilization
    Marginal costs
Estimate line benefits directly instead of operational costs