## Slide 1
Research Plan: The Transmission Expansion Planning Problem under the zero-carbon emission context
Erik F. Alvarez
Supervisors: Dr. Andrés Ramos Galán and Dr. Luis Olmos Camacho

## Slide 2
Reduction techniques of the problem size
Transmission grid modelling
Central and Local Flexibility
Model
Temporal reduction
  Representative stage (periods) with chronological interdependency
Search-space reduction
  Portfolio projects (decision variable clustering) based on game theory
AC-OPF within the TEP problem
  An improved linear AC-OPF model
    Based on the branch flow model
  A SOCP AC-OPF model
    Based on the Line-Wise model
  It allows us:
    Investment in Reactive power compensation
    To verify the accuracy and feasibility of the solution obtained
Central flexibility
  Management of hydro reservoirs, PSH, batteries, etc.
Local flexibility
  Demand-side management
  Bi-level model considering distribution grid and microgrids as well as local flexibility schemes.
Multi-stage transmission expansion planning
Hourly resolution
Storage management and investment

## Slide 3
Temporal reduction
  What data to use for it?
    Ex-ante or ex-post?
    correlations?
  Clustering
    Heuristic
    Optimization
  Relation between periods
    Transition matrices
Robustness of the clustering
  Multiple Scenarios
  Multiple periods
Stability of the representative periods
Stochastic multi-period transmission expansion planning with suitable representative periods

## Slide 4
Joint Research Work:
Introducing Learning Algorithms within an Operational State Aggregation Method for Power System Planning

## Slide 5: Problem Definition
  To solve our problems:
    Kristof: GEP with Representative Areas (Geographical aggregation considering weather area)
    Erik: TEP with Representative Weeks of 24 hours
      Considering AC-OPF (4-6 times of the TEP with DC-OPF)
*ESOM: Energy System Optimization Model
*GEP: Generation & Storage Expansion Planning
*TEP: Transmission Expansion Planning
*TSA: Time Series Aggregation

## Slide 6: State-of-the-art
Gaps:
A posteriori scheme or ex-port or Cost/Benefit oriented approach
Ordering and inter-periods links
Years data
Dynamic planning
Stochastic
The main feature of the paper:
[1], is related to compare TSA methods and GEP formulations which allow for long-term storage for the first time in an investment setting.
[3], is related to the unification of methods by Hilbers et al. and Teichgraeber et al.– which use operational variables in models without storage – with that of Kotzur et al.– which allow chronology-preserving aggregation for storage technologies.
[6], is related to the unification of the a priori and posteriori schemes.
[7], is related to consider the a posteriori scheme which uses the operation and investment cost.
*ESOM: Energy System Optimization Model
*GEP: Generation & Storage Expansion Planning
*TEP: Transmission Expansion Planning
*TSA: Time Series Aggregation
Notes: [1] Gonzato, Sebastian, Kenneth Bruninx, and Erik Delarue. "Long term storage in generation expansion planning models with a reduced temporal scope." Applied Energy 298 (2021): 117168.
[2] Pfenninger, Stefan. "Dealing with multiple decades of hourly wind and PV time series in energy models: A comparison of methods to reduce time resolution and the planning implications of inter-annual variability." Applied energy 197 (2017): 1-13.
[3] Hilbers, Adriaan P., David J. Brayshaw, and Axel Gandy. "Reducing climate risk in energy system planning: a posteriori time series aggregation for models with storage." Applied Energy 334 (2023): 120624.
[4] Kittel, Martin, Hannes Hobbie, and Constantin Dierstein. "Temporal aggregation of time series to identify typical hourly electricity system states: A systematic assessment of relevant cluster algorithms." Energy 247 (2022): 123458.
[5] Merrick, James H., John ET Bistline, and Geoffrey J. Blanford. "On representation of energy storage in electricity planning models." arXiv preprint arXiv:2105.03707 (2021).
[6] Zhang, Yuheng, et al. "A Model-Adaptive Clustering-Based Time Aggregation Method for Low-Carbon Energy System Optimization." IEEE Transactions on Sustainable Energy 14.1 (2022): 55-64.
[7] Sun, Mingyang, et al. "Data-driven representative day selection for investment decisions: A cost-oriented approach." IEEE Transactions on Power Systems 34.4 (2019): 2925-2936.
[8] Fazlollahi, Samira, et al. "Multi-objectives, multi-period optimization of district energy systems: I. Selection of typical operating periods." Computers & Chemical Engineering 65 (2014): 54-66.

## Slide 7
2017
2019
2023

## Slide 8: Keys & Gaps
Keys:
  Do we need to perform the problem size reduction? Yes! about 35 times more efficient – according to Ploussard, Q., et al.
      Ex-ante or ex-post? Ex-post! We got rich data from models
      Time consumption of the method? 60 min without considering the execution of the relaxed model and only 24 nodes!
Thus, We:
  Use of representative days/hours/weeks or non-homogenous sets of hours/days to reduce computational complexity of planning models
    For the selection of these representatives, clustering is usually performed over a large set of multi-dimensional input data.
  Use a relaxed version of the planning model (i.e., TEP with continuous variables) in the “a posteriori” scheme
    The relaxed version is usually executed per hour, day, or week but also for all the year in a deterministic planning approach.
Problems & Gaps:
  Considering a huge amounts of weather data, solving the relaxed model for all possible input days might still be computationally demanding
    Using a learning algorithm to approximate the outputs of the relaxed model
    Accuracy
    Scalability

## Slide 9: Gaps
From Literature:
  Do we need to perform the problem size reduction? Yes! about 35 times more efficient – according to Ploussard, Q., et al.
      Ex-ante or ex-post? Ex-post! We got rich data from models
      Time consumption of the method? 60 min without considering the execution of the relaxed model and only 24 nodes!
Thus, We:
  Use of representative days/hours/weeks or non-homogenous sets of hours/days to reduce computational complexity of planning models
    For the selection of these representatives, clustering is usually performed over a large set of multi-dimensional input data.
  Use a relaxed version of the planning model (i.e., TEP with continuous variables) in the “a posteriori” scheme
    The relaxed version is usually executed per hour, day, or week but also for all the year in a deterministic planning approach.
Problems & Gaps:
  Considering a huge amounts of weather data, solving the relaxed model for all possible input days might still be computationally demanding
    Using a learning algorithm to approximate the outputs of the relaxed model
    Accuracy
    Scalability

## Slide 10: Summary
From Literature:
  Do we need to perform the problem size reduction?
    Yes! about 35 times more efficient – according to Ploussard, Q., et al.
    Ex-ante or ex-post?
      Ex-post! We got rich data from models
    Time consumption of the method?
      60 min without considering the execution of the relaxed model and only 24 nodes!
GAPS
  Consider a huge amounts of weather data (scenarios or years)
  Use of learning algorithms to replace part or all the process of the determination of representatives.
    Increase accuracy and scalability

## Slide 11: Proposal: Part 1 Enhancing parts of the Operational State Aggregation Method using Learning Algorithms
Relaxed ESOM
Extract features
Clustering Method
Representative hours, days or system states
ESOM
Relaxed ESOM
Extract features
Clustering Method
Representative hours, days or system states
ESOM
Learning-assisted Optimization
Current proposal
Potential extension
Greedy ambition
*ESOM: Energy System Optimization Model
*GEP: Generation & Storage Expansion Planning
*TEP: Transmission Expansion Planning

## Slide 12: Learning-assisted optimization approaches
[1] Ruan, Guangchun, et al. "Review of learning-assisted power system optimization." CSEE Journal of Power and Energy Systems 7.2 (2020): 221-231.
Boundary Parameter Improvement (estimation of parameters in openTEPES):
  Improve the estimation of these parameters to get a more accurate feasible regions
    Deep learning approach
    Multivariate clustering technique + recurrent neural network
Optimization Option Selection (initial values of variables in openTEPES):
  Boost the optimization performance by selecting better options (estimation) (e.g., initial values, on/off status)
    Neural Networks
Surrogate Model
  Replace optimization or control models
    Reinforcement learning
      Markov decisions
    Deep reinforcement learning
Hybrid Model
  Combine machine learning approaches and optimization model to boost the overall performance
  Iterative structure
  Coupled structure that embeds a learning models
    Neural networks

## Slide 13: Surrogate Models -> Hybrid Models

## Slide 14: Proposal: Learning approaches
Deep learning:
  It is a subfield of machine learning that uses neural networks with many layers to learn hierarchical representations of data. Deep learning has revolutionized many areas of AI, including computer vision, natural language processing, and speech recognition.
  Pros:
    Deep learning can learn complex patterns in data that are difficult to capture with traditional machine learning models.
    It can handle high-dimensional data.
  Cons:
    Deep learning models can be computationally expensive to train.
    They require large amounts of data to achieve good performance.
    They can be prone to overfitting.
Reinforcement learning:
  It is a type of machine learning that involves an agent learning to make decisions by interacting with an environment. The agent receives rewards or penalties based on its actions, and its goal is to maximize its cumulative reward over time.
  Pros:
    Reinforcement learning can be used for tasks where there is no labeled training data.
    It can learn to make decisions in complex environments with long-term dependencies.
  Cons:
    Reinforcement learning can be computationally expensive to train.
    It requires careful tuning of hyperparameters and reward functions.
    It can be prone to instability during training.
Deep reinforcement learning:
  It combines reinforcement learning with deep learning, allowing the agent to learn complex representations of its environment. Deep reinforcement learning has achieved state-of-the-art performance in many domains, including playing video games and controlling robots.
  Pros:
    Deep reinforcement learning can learn complex strategies in environments with high-dimensional state spaces.
    It can learn from raw sensory input, without the need for hand-engineered features.
  Cons:
    Deep reinforcement learning can be computationally expensive to train.
    It requires careful tuning of hyperparameters and reward functions.
    It can be prone to instability during training, especially when using function approximators like neural networks.
[1] Ruan, Guangchun, et al. "Review of learning-assisted power system optimization." CSEE Journal of Power and Energy Systems 7.2 (2020): 221-231.

## Slide 15: Neural Networks
[1] Chen, Xin, et al. "Reinforcement learning for selective key applications in power systems: Recent advances and future challenges." IEEE Transactions on Smart Grid (2022).
Neural network:
  It can be used for a variety of tasks, such as image classification, natural language processing, and time series prediction.
  Neural networks are used to approximate the optimal action-value or state-value function, which determines the expected reward that the agent will receive for each action in a given state.
  Pros:
    Neural networks can learn complex nonlinear relationships between inputs and outputs.
    They can be used for a wide range of applications.
    They can handle high-dimensional data.
  Cons:
    Neural networks can be computationally expensive to train.
    They require large amounts of data to achieve good performance.
    They can be prone to overfitting.
Multi-layer perceptron (MLP):
  A feedforward neural network with multiple layers of fully connected neurons. MLPs are often used for function approximation in reinforcement learning.
Convolutional neural network (CNN):
  A neural network designed for processing inputs that have a grid-like topology, such as images. CNNs are often used for visual perception tasks in reinforcement learning.
Recurrent neural network (RNN):
  A neural network with feedback connections that allow it to process sequences of inputs. RNNs are often used for tasks that involve temporal dependencies in reinforcement learning.
Long Short-Term Memory (LSTM):
  A type of RNN that is designed to capture long-term dependencies in sequential data. LSTMs are often used for tasks that require memory in reinforcement learning.
Transformer Network (TN):
  The Transformer Neural Network is a novel architecture that aims to solve sequence-to-sequence tasks while handling long-range dependencies with ease. It was proposed in the paper “Attention Is All You Need” 2017.

## Slide 16: Research Plan

## Slide 17: Understanding Neural Networks: Forecasting example

## Slide 18
Considering multiple layers, lead us to the usage of a significant number of neurons.
A randomly dropping out with a probability between 10% and 30% leads us to a best performance on the validation set.
A small penalty term (0.0001-0.001) in weight decay regularization also leads us to a best performance.
A common practice is to use a grid search or random search to explore a range of hyperparameter values and select the one that gives the best performance on a validation set.
Understanding Neural Networks: Observations
Optimal number of neurons
Regularization techniques (Hyperparameters)
  Dropout
  Weight Decay
Observations
Tests:

## Slide 19: Understanding Neural Networks: Optimal Number of Neurons
NN: 1 hidden layer, 100 epochs
NN: 2 hidden layer, 100 epochs

## Slide 20: Understanding Neural Networks: Regularization technique - Dropout
Dropout is a regularization technique used to prevent overfitting in neural networks. It works by randomly dropping out with a certain probability (setting to zero) some neurons during training, which forces the remaining neurons to learn more robust features.
NN: 1 hidden layer, 100 epochs, Dropout: 00%
Dropout: 10%
Dropout: 40%
Dropout: 60%
Dropout: 20%

## Slide 21: Understanding Neural Networks: Regularization technique - Weight Decay
Weight decay is a regularization technique used to prevent overfitting in neural networks by adding a penalty term to the loss function that encourages the weights to be small.
NN: 1 hidden layer, 100 epochs, no weight decay
Weight decay: 0.0001
Weight decay: 0.01
Weight decay: 0.1
Weight decay: 0.001

## Slide 22
Considering multiple layers, lead us to the usage of a significant number of neurons.
A randomly dropping out with a probability between 10% and 30% leads us to a best performance on the validation set.
A small penalty term (0.0001-0.001) in weight decay regularization also leads us to a best performance.
A common practice is to use a grid search or random search to explore a range of hyperparameter values and select the one that gives the best performance on a validation set.
Understanding Neural Networks: Observations
To explore two more regularization techniques:
  L1 and L2 regularization
  Data augmentation
ToDo:

## Slide 23: DC-Optimal Power Flow via an ANN
Ingredients
Process
Requirements
The trained model should be able to solve the OPF problem in less than 1 second.
The model must not violate any of the constraints of the problem.
Training database
Training algorithm
Test database
Data collection
Data pre-processing
Model training
Model testing
Model deployment
The increase in the total objective cost function from the traditional lengthy OPF solvers must not exceed 5%.
Performance Metrics
A: Mean squared error
B: True positive rate (TP/(TP+FN))
C: True negative rate (TN/(TN+FP))
D: Positive predictive value (TP/(TP+FP))
E: Harmonic mean of Precision and Recall (B*D/(B+D))
F: MCC (Matthews correlation coefficient) (TP*TN-FP*FN)/((TP+FP)(TP+FN)(TN+FP)(TN+FN))^0.5
TP: True positive
FP: False positive
FN: False negative
TN: True Negative

## Slide 24: DC-Optimal Power Flow via an ANN
1
3
2

## Slide 25: DC-Optimal Power Flow via an ANN
Mathematical Formulation
Objective function: |  |  | (1.1)
 | Subject to: |  | 
eBalance |  |  | (1.2)
eKirchhoff2ndLaw1 |  |  | (1.3)
Bounds on generation |  |  | (1.4) (1.5)
Bounds on network |  |  | (1.6) (1.7)
Objective function: |  |  | (1.1)
 | Subject to: |  | 
eBalance |  |  | (1.2)
eKirchhoff2ndLaw1 |  |  | (1.3)
Bounds on generation |  |  | (1.4) (1.5)
Bounds on network |  |  | (1.6) (1.7)

## Slide 26: DC-Optimal Power Flow via an ANN
NN
Parameters
Continuous
Discrete
Outputs
Electricity demand
Wind & solar profiles
Bounds
Network features
Generation costs
Variables
Power flows
Power generation
Dual variables
Phase 1:
Normalized demand, and generation
Dataset
Phase 2:
Normalized demand, network features, wind & solar profiles, generation, power flows, and dual variables
Inputs
Outputs

## Slide 27: DC-Optimal Power Flow via an ANN
Phase 1:
Normalized demand and generation
NN’s architecture
3
32
16
8
3
Hidden layers
Tune up the hyperparameters
ToDo:

## Slide 28: DC-Optimal Power Flow via an ANN
Phase 1:
Normalized demand and generation

## Slide 29: Proposal Operational State Aggregation Method Based on Benefits using Learning Algorithms
Relaxed ESOM
Extract features
Clustering Method
Representative periods
ESOM
Extract features
Current proposal
Potential extension
Greedy ambition
*ESOM: Energy System Optimization Model
**Encoder for dimension reduction
Input Data
ANN
Estimator
Total benefit per asset in hourly basis
ANN
Encoder**
Clustering Method
Representative Periods
Relaxed ESOM
Results

## Slide 30: Proposal Operational State Aggregation Method Based on Benefits using Learning Algorithms
Input Data
Extract features (Dimension reduction)
Clustering Method
Representative periods
ESOM
Features
(Benefits)
Relaxed ESOM
Current proposal
Potential extension
*ESOM: Energy System Optimization Model
**Encoder for dimension reduction
NN1
Estimation
NN2
Classification
K-means/
K-medoids
3*S*T*N*L^2

## Slide 31: Proposal - Part 1: How to get the total benefit?
*ESOM: Energy System Optimization Model
*PINT: Put IN one at a Time
*TOOT: Take Out One at a Time
Relaxed ESOM
in hourly basis
Economic Dispatch
in hourly basis
ANN
Estimator
ANN
Estimator
Benefit per asset in hourly basis
PINT Sequence
Relaxed ESOM
in hourly basis
Economic Dispatch
in hourly basis
ANN
Estimator
ANN
Estimator
Benefit per asset in hourly basis
TOOT Sequence
Sequence per candidate asset
Total benefit per candidate asset in hourly basis
The PINT and TOOT approaches

## Slide 32: Research Plan
  Stage 0: Understanding neural networks
    Develop a neural
    Literature Review:
      Review of learning-assisted approaches
      Review of learning-assisted power system optimization
      Review of neural networks
    Using Python and PyTorch (Ruben’s suggestion), steps:
      First, install PyTorch. (You can follow the official PyTorch installation guide for this).
      Once you have installed PyTorch, you can validate the installation by running a small program in PyTorch as a non-root user 1. This will ensure that PyTorch has been installed correctly.
      After validating the installation of PyTorch, you can start using it for image classification . You can also learn about tensors, datasets and dataloaders, transforms, building models, automatic differentiation, optimization loop, saving/loading and using models from the official PyTorch tutorials.
  Step 2:
    Design my own IA-based method.

## Slide 33: Proposal: Part 2
[1] Chen, Xin, et al. "Reinforcement learning for selective key applications in power systems: Recent advances and future challenges." IEEE Transactions on Smart Grid (2022).
RL schemes for the control and decision-making in power systems (figure taken from [1]).

## Slide 34: A Learning-Assisted Optimization Model for Power System Planning
Motivation
Traditional solvers are slow - fast approximate solvers needed
Method
Experiments
Application
Economic Dispatch
Expansion planning problem with continuous variables